## Slide 1: Introduction Chapter 1
  Uses of Computer Networks
  Network Hardware
  Network Software
  Reference Models
  Example Networks
  Network Standardization
  Metric Units
Revised: August 2011
Notes: Gray units can be optionally omitted without causing later gaps

## Slide 2: Uses of Computer Networks
Computer networks are collections of autonomous computers, e.g., the Internet
They have many uses:
  Business Applications »
  Home Applications »
  Mobile Users »
These uses raise:
  Social Issues »
This text covers networks for all of these uses
Notes: Contrast computer networks with distributed systems, in which a model on top of the network is used to present the independent computers to users as a single coherent system, e.g., the Web.

## Slide 3: Business Applications
request
response
Companies use networks and computers for resource sharing with the client-server model:
Other popular uses are communication, e.g., email, VoIP, and e-commerce
Notes: Resource sharing was initially about physical resources, such as printers, but is now often about access to information, such as a file server.
The Web is an example of client-server computing.

## Slide 4: Home Applications
Homes contain many networked devices, e.g., computers, TVs, connected to the Internet by cable, DSL, wireless, etc.
Home users communicate, e.g., social networks, consume content, e.g., video,
Some application use the peer-to-peer model in which there are no fixed clients and servers:
Notes: P2P contrasts with client-server. Why is it under home applications? Because unlike cloud there is no need to have a business run dedicated infrastructure for the app to work.

## Slide 5: Network Hardware
Networks can be classified by their scale:
Scale | Type
Vicinity | PAN (Personal Area Network) »
Building | LAN (Local Area Network) »
City | MAN (Metropolitan Area Network) »
Country | WAN (Wide Area Network) »
Planet | The Internet (network of all networks)
Notes: An “internetwork” is any larger network made up of smaller component networks. The “Internet” (with a capital I) is the set of all connected networks.

## Slide 6: Personal Area Network
Connect devices over the range of a person
Example of a Bluetooth (wireless) PAN:

## Slide 7: Local Area Networks
Connect devices in a home or office building
Called enterprise network in a company
Wireless LAN
with 802.11
Wired LAN with
switched Ethernet

## Slide 8: Metropolitan Area Networks
Connect devices over a metropolitan area
Example MAN based on cable TV:
Notes: This is a common way in which home subscribers obtain access to the Internet in the US.

## Slide 9: Wide Area Networks (1)
Connect devices over a country
Example WAN connecting three branch offices:
Notes: The company probably leases the transmission lines (since most companies do not have their own lines).

## Slide 10: Wide Area Networks (2)
An ISP (Internet Service Provider) network is also a WAN.
Customers buy connectivity from the ISP to use it.
Notes: Now the company/customer buys service from an ISP who uses its own lines to deliver packets.

## Slide 11: Wide Area Networks (3)
A VPN (Virtual Private Network) is a WAN built from virtual links that run on top of the Internet.
Notes: Now the company/customer uses the Internet (might be multiple ISPs) for connectivity. The links are virtual in the sense that they refer to some path via the Internet rather than a particular transmission line.

## Slide 12: Network Software
  Protocol layers »
  Design issues for the layers »
  Connection-oriented vs. connectionless service »
  Service primitives »
  Relationship of services to protocols »

## Slide 13: Protocol Layers (1)
Protocol layering is the main structuring method used to divide up network functionality.
Each protocol instance talks virtually to its peer
Each layer communicates only by using the one below
Lower layer services are accessed by an interface
At bottom, messages are carried by the medium

## Slide 14: Protocol Layers (2)
Each lower layer adds its own header (with control inform-ation) to the message to transmit and removes it on receive
Layers may also split and join messages, etc.

## Slide 15: Design Issues for the Layers
Each layer solves a particular problem but must include mechanisms to address a set of recurring design issues
Issue | Example mechanisms at different layers
Reliability despite failures | Codes for error detection/correction Routing around failures
Network growth and evolution | Addressing and naming Protocol layering
Allocation of resources like bandwidth | Multiple access Congestion control
Security against various threats | Confidentiality of messages Authentication of communicating parties
Notes: The point is that there are some issues that are not wholly the responsibility of any one layer, and they crop up again and again in the text. For example, reliability is often considered a key function of the transport layer (i.e., making transport reliable) yet reliability mechanisms also appear in other layers (error codes in the link layer, routing around failures in the network layer, and replication at the application layer).

## Slide 16: Connection-Oriented vs. Connectionless
Service provided by a layer may be kinds of either:
  Connection-oriented, must be set up for ongoing use (and torn down after use), e.g., phone call
  Connectionless, messages are handled separately, e.g., postal delivery
Notes: TCP provides a reliable bytestream service at the Transport layer, IP provides unreliable datagram service at the Network layer.
More examples: RTP (used to carry VoIP data) provides unreliable connection service; 802.11 (WiFi) provides acknowledged datagram service; Ethernet provides unreliable datagram service.

## Slide 17: Service Primitives (1)
A service is provided to the layer above as primitives
Hypothetical example of service primitives that may provide a reliable byte stream (connection-oriented) service:

## Slide 18: Service Primitives (2)
Hypothetical example of how these primitives may be used for a client-server interaction
Client
Server
LISTEN (0)
ACCEPT
RECEIVE
SEND (4)
DISCONNECT (6)
CONNECT (1)
SEND
RECEIVE
DISCONNECT (5)
Connect request
Accept response
Request for data
Reply
Disconnect
Disconnect
(2)
(3)
Notes: The primitives are called at the client and server by the higher layer using the service. The layer implements the primitives by sending messages using the services of the lower layer; these messages are assumed to be reliable for simplicity and the lower layer service is not otherwise described.
This is similar to the way that simple Web browsers and Web servers work today.

## Slide 19: Relationship of Services to Protocols
Recap:
  A layer provides a service to the one above [vertical]
  A layer talks to its peer using a protocol [horizontal]

## Slide 20: Reference Models
Reference models describe the layers in a network architecture
  OSI reference model »
  TCP/IP reference model »
  Model used for this text »
  Critique of OSI and TCP/IP »

## Slide 21: OSI Reference Model
A principled, international standard, seven layer model to connect different systems
– Provides functions needed by users
– Converts different representations
– Manages task dialogs
– Provides end-to-end delivery
– Sends packets over multiple links
– Sends frames of information
– Sends bits as signals

## Slide 22: Functions Layers Perform
Physical layer implements a digital communication link that deliver bits.
Data link layer implements a packet delivery service between nodes that are attached to the same physical link.
Network layer guides the packets from their source to their destination, along a path that may comprise a number of links.
Transport layer supervises the end-to-end transmission of packets. This layer may arrange for retransmission of erroneous packets.

## Slide 23: Functions Layers Perform
Session layer users the transmission layer services to set up and supervise connections between end systems.
Presentation layer takes care of data compression, security, and format conversions so that nodes that user different representations of information can communicate efficiently and securely.
Application layer implements commonly used communication services including file transfer, directory services, virtual terminal.

## Slide 24: Model Used
It is based on the TCP/IP model but we call out the physical layer and look beyond Internet protocols.

## Slide 25: Internet Layers
LAN or link layer: Transmitting packets on one link or across interconnected LANs.
Network layer: Transmitting messages on a sequence of links from one terminal node to another.
Transport layer: Supervising the transmission of messages from end to end.
Application layer: Providing a number of communication services for the users, including file transfer, remote terminal, electronic mail, and directory services.

## Slide 26: Design Questions
A number of questions must be resolved to ensure effective use of network resources, and at same time to guarantee the quality of service to users.
(a) Routing: what paths should the packets follow in the network?
(b) Flow Control: How can one regulate the flow so as to avoid having parts of the network become congested?
(c) Access Control: How can one monitor and control the traffic actually generated by the call to ensure it conforms to the traffic descriptors originally specified?
(d) Admission Control: Given a call arriving, requiring a connection with specified quality of service (QoS) [Bandwidth, loss probability, delay, etc.] should it be admitted?

## Slide 27: Design Questions
(e) Management: How can one supervise the operations of a network so as to provide timely and relevant information for detecting and correcting faulty operations and for long-term network planning?
(f) Security: How can the privacy of the information transmitted over the network and the integrity of the nodes of the network be maintained ?
(g) Error Control: How can the network automatically correct errors that occur during packet transmissions?
(h) Addressing: what is a convenient way of specifying the addressing of the terminal nodes?

## Slide 28: Design Questions
(i) Standards: How can the characteristics of the nodes be described so that vendors can build compatible hardware and software?
(j) Presentation: How can one enable many different types of terminal equipment to communicate?

## Slide 29: Example Networks
  The Internet »
  3G mobile phone networks »
  Wireless LANs »
  RFID and sensor networks »

## Slide 30: Internet (1)
Before the Internet was the ARPANET, a decentralized, packet-switched network
ARPANET topology in Sept 1972.
Nodes are early routers, linked to hosts
56 kbps links
Notes: Decentralized or fully distributed is a contrast to the hierarchical telephone network that came beforehand. Unlike the telephone network, blowing up a single important node will not break the network or large portions of it.

## Slide 31: Internet (2)
The early Internet used NSFNET (1985-1995) as its backbone; universities connected to get on the Internet
NSFNET topology in 1988
T1 links (1.5 Mbps)
Notes: NSFNET was an academic research network growing out of CSNET that was created so that universities without DoD contracts could participate. It was initially connected to the ARPANET by gateways, and later took over the central role as the “backbone of the Internet”, i.e., the network through which packets passed on their way between parties connected to different parts of the Internet.

## Slide 32: Internet (3)
The modern Internet is more complex:
  ISP networks serve as the Internet backbone
  ISPs connect or peer to exchange traffic
  Within each network routers switch packets
  Between networks, traffic exchange is set by business agreements
  Customers connect at the edge by many means
    Cable, DSL, Fiber-to-the-Home, 3G/4G wireless, dialup
  Data centers concentrate many servers (“the cloud”)
  Most traffic is content from data centers (esp. video)
  The architecture continues to evolve
Notes: ISP = Internet Service Provicer, IXP = Internet eXchange Point

## Slide 33: Internet (4)
Architecture of the Internet

## Slide 34: 3G Mobile Phone Networks (1)
3G network is based on spatial cells; each cell provides wireless service to mobiles within it via a base station

## Slide 35: 3G Mobile Phone Networks (2)
Base stations connect to the core network to find other mobiles and send data to the phone network and Internet

## Slide 36: 3G Mobile Phone Networks (3)
As mobiles move, base stations hand them off from one cell to the next, and the network tracks their location
Handover

## Slide 37: Wireless LANs (1)
In 802.11, clients communicate via an AP (Access Point) that is wired to the rest of the network.

## Slide 38: Wireless LANs (2)
Signals in the 2.4GHz ISM band vary in strength due to many effects, such as multipath fading due to reflections
    requires complex transmission schemes, e.g., OFDM

## Slide 39: Wireless LANs (3)
Radio broadcasts interfere with each other, and radio ranges may incompletely overlap
    CSMA (Carrier Sense Multiple Access) designs are used
Notes: Both broadcast and different ranges are complications that do not exist for point-to-point wired links.

## Slide 40: RFID and Sensor Networks (1)
Passive UHF RFID networks everyday objects:
    Tags (stickers with not even a battery) are placed on objects
    Readers send signals that the tags reflect to communicate

## Slide 41: RFID and Sensor Networks (2)
Sensor networks spread small devices over an area:
    Devices send sensed data to collector via wireless hops

## Slide 42: Network Standardization
  Standards define what is needed for interoperability
  Some of the many standards bodies:
Body | Area | Examples
ITU | Telecommunications | G.992, ADSL H.264, MPEG4
IEEE | Communications | 802.3, Ethernet 802.11, WiFi
IETF | Internet | RFC 2616, HTTP/1.1 RFC 1034/1035, DNS
W3C | Web | HTML5 standard CSS standard

## Slide 43: Metric Units
The main prefixes we use:
  Use powers of 10 for rates, powers of 2 for storage
    E.g., 1 Mbps = 1,000,000 bps, 1 KB = 1024 bytes
  “B” is for bytes, “b” is for bits
Prefix | Exp. | prefix | exp.
K(ilo) | 103 | m(illi) | 10-3
M(ega) | 106 | μ(micro) | 10-6
G(iga) | 109 | n(ano) | 10-9
Notes: You’ll also see kbps and KB. The lowercase k in kbps is for historical reasons.

## Slide 44: End
Chapter 1