## Slide 1: OFDMA Networks (Physical and MAC)
By Dr. Mohamad Awad

## Slide 2: Outline
  Wireless channel impairments and their effect on wireless communication
Channel modeling
  Sounding technique
OFDM as a solution
OFDMA as an improved solution
MIMO-OFDMA
Conclusion

## Slide 3: Propagation Mechanisms in wireless channels
Reflection
Diffraction
Scattering
Indoor wireless channel
Outdoor wireless channel
Transmitter
Receiver
Three propagation mechanisms in two types of propagation channels

## Slide 4: Large Scale Fading
Topographic and elevation data were obtained from Natural
resources Canada.

## Slide 5: Large-Scale Fading Vs. Small-Scale Fading
Figure taken from :”Wireless communication, principle and practice” by T. S. Rappaport
Transmitter – Receiver Separation
Received Power
Large-Scale Fading
Small-Scale Fading
Coherent Summation of 2 multipaths
Incoherent Summation of 2 multipaths
Partly- Coherent Summation of 2 multipaths
Im
Re
Im
Im
Re
Re

## Slide 6: Channel-Sounding
Propagation mechanisms:
- Reflection.
Diffraction.
Scattering.
Measurement setting:
- frequency.
- line-of-sight vs no-line-of-sight.
- environment.
- transmitter - Receiver separation.
- human presence.
- floor Area.
- extent of Clutters.
- detection Threshold.
Propagation Channel
Receiver
Channel Impulse Response Power
Transmitter
power
time
?

## Slide 7: Channel Impulse-Response
Total number of multipaths
n-th multipath excess delay
n-th multipath amplitude
excess delay
Receiver Detection
Threshold
Excess Delay (ns)
Normalized Received Power (dB)

## Slide 8: Review: Convolution
http://www.jhu.edu/signals/convolve/

## Slide 9: Frequency-Flat Vs. Frequency-Selective Fading
Channel
Transmitted Signal
Received Signal
Frequency-Flat Fading
Frequency
Bs @ Tx
Bs @ Rx
Bw
Bs << Bw
Ts @ Tx
time
Ts >>
No Time Dispersion
@ Rx
Ts @ Tx
time
ISI
Ts <<
Time Dispersion and ISI
Frequency-Selective Fading
Frequency
Bw
Bs >> Bw
Bs @ Tx
Bs @ Rx

## Slide 10: Multicarrier Transmission

## Slide 11: History of Multicarrier transmission
A principle for multi-channel transmission over a bandlimited channel was proposed in 1966 !!
Why did take that long to be implemented?
Combine ?
DFT !

## Slide 12: What is OFDM?
Orthogonal Frequency Division Multiplexing
Method to multiplex many “narrowband” signals into an aggregate “wideband” data stream
Normally, the subcarriers would need sufficient separation to avoid adjacent channel interference
OFDM uses orthogonal (1/Tsym) subcarrier spacing to maintain subcarrier separation

## Slide 13: Orthogonality

## Slide 14: Orthogonal Carrier Spacing
0
5
10
15
20
25
30
-0.4
-0.2
0
0.2
0.4
0.6
0.8
1
1.2
1/Tsym

## Slide 15: OFDM System Model

## Slide 16: OFDM-TDMA MAC
Sub-2
Sub-1
Sub-4
Sub-3
Sub-5
Frequency
Time
User 2
User 1
User 4
User 3
High latency, # users large
In-effecient power usage
In-effecient in frequency utilization
Disadvantages
Easy implementation
Simple resource allocation
Low processing requirement
Low signaling overhead (channel gain)
Advantages
0
5
10
15
20
25
30
-0.4
-0.2
0
0.2
0.4
0.6
0.8
1
1.2

## Slide 17: Applications

## Slide 18: Multi-user diversity

## Slide 19: Time Varying Channel
τex
Transmitter
Time
τex
τex
The channel is generally time varying due to:
  User changes location.
  Object gets between the transmitter and receiver (bus)

## Slide 20: OFDMA
Orthogonal Frequency Division Multiple Access.
A subcarrier is exclusively assigned to a user.
Exploits multiuser diversity.
Dynamic subcarrier assignment
Sub-2
Sub-1
Sub-4
Sub-3
Sub-5
Frequency
Time
User 2
User 1
User 4
User 3
High latency, # users large
In-effecient power usage
In-effecient in frequency utilization
Disadvantages of OFDM

## Slide 21: OFDMA Resource Allocation
Base Station ( BS )
User # 1
User # 2
Internet
Allocated subcarriers
Trans Power
Channel gain
QoS (rate, dropping rate, etc..)
Time
Freq
Maximize Throughput
Assign power < Max
Each subcarrier is exclusively assigned
Guarantee QoS
New
gains

## Slide 22: OFDMA MAC
Sub-2
Sub-1
Sub-4
Sub-3
Sub-5
Frequency
Time
User 2
User 1
User 4
User 3
Disadvantages
Complicated Res. Alocation
Signaling overhead (adaptive scheme)
Advantages
Simple implementation
Resource allocation flexibility
Adaptation to channel characteristics (adaptive scheme)
Better BER performance (adaptive scheme)

## Slide 23: Space Diversity
Two antennas separated by several wavelengths will not generally experience fades at the same time
“Space Diversity” can be obtained by using two receiving antennas and switching instant-by-instant to whichever is best
Signal received by Antenna 1
Signal received by Antenna 2
Combined Signal
D

## Slide 24: MIMO systems

## Slide 25: MIMO
Basic idea of MIMO: Improve quality (BER) and/or data
rate (bits/sec) by using multiple TX/RX antennas
Core scheme of MIMO: space-time coding (STC)
Two main functions of STC: diversity & multiplexing

## Slide 26: MIMO - OFDMA

## Slide 27: Conclusion
Wireless channel suffers from large scale fading and small scale fading
After modeling the channel, communication systems are matched to the channel.
OFDMA is one of advanced technologies to overcome the wireless channel impairments.
OFDMA can be combined with MIMO to improve performance .

## Slide 28: Questions
????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????
????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????Questions???????????????????????????????
????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????
????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????????